## Slide 1: ΣΦΗΜΜΥ 12 Workshop Εισαγωγή στη ROS: Δημιουργία μοντέλου και αυτόνομη χαρτογράφηση
-Μηνάς Κοσμίδης
Φοιτητής Ηλ. Μηχ.
-Σωτήρης Μπαρλάκας
Φοιτητής Μηχ. Μηχ

## Slide 2: What is?
Open source
Meta-operating system
Real-time Framework
Operating System Services
Robot Operating System

## Slide 3: Before ROS…
Lack of standards
Little code reusability
Keeping re-coding:
Device drivers,
Standard algorithms,
Access to robot’s interfaces,
Management of onboard processes
….reinventing the wheel every time a new robot is built

## Slide 4: So what is ROS?
“ROS is an open-source, meta-operating system for your robot”
http://wiki.ros.org/ROS/Introduction

## Slide 5: Why?
Open source
Big Community
Rich documentation
Already implemented packages
Language-agnostic
General and reusable

## Slide 6: Robots that run ROS
From academia…
… to the Industry
And many others….

## Slide 7: Our Robot
Differential-Drive Robot
Chassis
Right_wheel
Left_wheel
Caster_wheel
Laser_sensor
Right_rim
Camera_sensor

## Slide 8: How does ROS work?
ROS Master
Topics
Nodes
Messages
Actions & Services
Publishers & Subscribers
‘’ROS systems consist of many small programs (nodes) which
connect to each other and continuously exchange messages’’

## Slide 9: Publishers & Subscribers
Subscriber
Publisher
Topic
Message:
string ‘’It’s a secret!’’
Nodes
Subscribers
(receive data)
Publishers
(sending data)
Ex.
float64 temperature
Messages

## Slide 10: How Nodes communicate?
Camera publishes to “/images” topic
Image Viewer subscribes to “/images” topic
Master notifies Camera and Image viewer about each other’s existence so communication begins

## Slide 11: What about topics?
Subscriber 1
“I want to catch up
on some gossip”
Publisher
Topic 1: /gossip
Message:
string ‘’It’s a secret!’’
Subscriber 2
“I want to catch up on some gossip”
Topic 2: /alien_voices
Subscriber 3
“I want to communicate with aliens”

## Slide 12: How differential plugin works?
Differential Drive Robot
It receives (subscriber) the desired linear (v) and angular (ω) velocities and calculates wheel rotation velocity
Geometry_msgs/Twist
It subscribes for messages of type:
(to the specified topic)
It also publishes odometry data..
(to another topic)

## Slide 13: How LIDAR plugin works?
sensor_msgs/LaserScan
It publishes messages of type: (to the specified topic)
Ranges is an array with the distances [m] that each ray traveled until it reflects back by an obstacle

## Slide 14: The importance of transformations
The measurements of the Lidar have to be transformed to the base_link frame for localization.
Same principle for mapping...
5 m
base frame
lidar

## Slide 15: Our code architecture